## Slide 1: Role of charge trapping in GaN devices for a long hi-rel space mission
GaN RF/microwave devices ---
  mainly useful as power amplifiers
  traps manifest
    “current collapse”
    pulse-to-pulse instability
    linear mode gain degradations much greater than in saturation
GaN power switch devices ---
  mainly useful in switching power supplies
  traps manifest as
    changing dynamic drain-source on-resistance RDS(on)
    RDS(on) increases over time in a long mission
    gradual loss of efficiency
    “negative” effective activation energy effect
All of these effects are caused by temporary electron trapping
  Have reliability metrics for GaN devices fallen short?
  Is the space community adopting GaN too quickly?
CMSE 2021 panel discussion