## Slide 1
Alternate Grade Parts for Space
Commercialization of Military and Space Electronics Conference
Mark Porter
20 April, 2021
© 2021 California Institute of Technology. Government sponsorship acknowledged.

## Slide 2: Need for Alternate Grade Parts Task Group
Short Duration Small Satellite Missions
  Higher Quantities of Modest Capability Satellites
  On-Orbit Redundancy and Sparing
Greater Diversity of EE Device Types in Alternate Grade Markets
Faster Lead Times for Alternate Grade EEE Devices
Lower Cost for Alternate Grade EEE Devices
Task Group Charter - Create A Guideline Or Checklist To Use When Considering The Use Of Any Alternate Grade Parts For A Space Application.
  Military Specifications Tend To Be Very Prescriptive Describing Every Step And Process
  That Was Basis For Modern Electronics Industry
    Manufacturers Have Figured Out Ways To Achieve High Reliability In Their Own Ways
  Understand Types of Missions That Might Consider Alternate Grade EEE Devices
© 2021 California Institute of Technology. Government sponsorship acknowledged.

## Slide 3: Items To Consider
Manufacturer Related Questions
  How Does The Manufacturer Address Infant Mortality?
    Do They Test To Weed Out Weaker Devices?
    Do They Perform Some Sort of HALT/HASS Test to Ensure a Robust Design?
    Do They Control Their Processes To Ensure Low Infant Mortality Escapes?
  How Does The Manufacturer Ensure Long Life at Rated Conditions?
    Does The Manufacturer Have Oodles of Life Test Data?
    Does The Manufacturer Perform Periodic Life Testing to Ensure Process Stability?
  How Does The Manufacturer Ensure Consistency From Part Lot to Part Lot?
    Does The Manufacturer Trend Statistics And How Often?
  Part Performance After Exposure to Expected Radiation Environment
    Are Wafers All Produced The Same Way With The Same Materials?
  Part Capability Over Expected Mission Temperature Range
Mission Related Questions
  Cost To Orbit Considerations
  Is There On Orbit Satellite Redundancy?
  Can Failed Satellites Be Quickly Replenished?
  Are We Just Trying To Demonstrate Something One Time?
© 2021 California Institute of Technology. Government sponsorship acknowledged.

## Slide 4
© 2021 California Institute of Technology. Government sponsorship acknowledged.